## T80a Description
Configurable cpu core that supports Z80, 8080 and gameboy instruction sets. Z80 and 8080 compa­bility have been proven by numerous implementations of old computer and arcade systems. It is used in the zxgate project, a zx81, zx spectrum, trs80 and Jupiter ACE clone project. And also in the FPGA Arcade project. A Z80 SoC debug system with ROM, RAM and two 16450 UARTs is inclu­ded in the distribution. It is possible to run the NoICE debugger on this system. Batch files for runn­ning XST and Leonardo synthesis can be found in syn/xilinx/run/. Check these scripts to see how to use the included VHDL ROM generators. Before you can run the scripts you need to compile he­x2rom and xrom or download binaries from here. You must also replace one of the hex files in sw/ or change the batch files to use another hex file. The z88dk C compiler can be used with T80. The "embedded" configuration can be used with the debug system without modifications. Browse sour­ce code here. Download latest tarball here. Thanks to MikeJ for some serious debugging and to the zxgate project members for invaluable Z80 information.
## Features
- Technology independent
- Up to 35MHz clock in Spartan2 -5 using XST synthesis
- 10k gates and up to 100MHz in 0.18 CMOS
- Supports all undocumented Z80 instructions
- Supports all Z80 interrupt modes
- Correct R register behaviour
- Correct Z80 instruction timing
- Almost 100% correct behavior of the undocumented Z80 flags
- Both a synchronous (for implementation) and an asynchronous (for board level simulations) Z80 top level
- Only a synchronous 8080 top level
## Status
- Z80 compability and functionality thoroughly verified in FPGA
- The gameboy mode is experimental
- No gameboy top level